## Slide 1: Revolutionize our understanding of the transient universe: 20 years of discovery in Swift
T. Sakamoto (AGU)

## Slide 2: Outlines
Swift for dummies
Neil Gehrels
Swift’s discoveries
Unique capabilities of Swift
High redshift GRBs
[Smallsat development at AGU]
Future of Swift

## Slide 3: Swift for dummies

## Slide 4: Breaf history of Swift
NASA’s Medium-class Explorer (MIDEX)
  January 1999: Selection for phase-A study
  October 1999: Mission selection
  November 2004: Launch
20 years and still counting ….
Swift/BAT team (around 2005?)
Scott
Jack
Hans
Me
Craig
Jay
Ann
Masaya
Goro
Derek
Nakazawa-san

## Slide 5: Swift satellite
Burst Alert Telescope (BAT)
GRB detection and localization (~1 – 4 arcmin)
X-Ray Telescope (XRT)
X-ray afterglow (~5 arcsec)
Detection of X-ray afterglow for ~90% of GRB
UV/Optical Telescope (UVOT)
UV/optical afterglow (~0.5“)
Detection of UV/optical afterglow for ~60% of GRBs
Boeing Delta II rocket: November 20, 2004
Altitude : 600 km
Mass : 1270 kg

## Slide 6: BAT (Burst Alert Telescope)
Energy range: 15-150 keV
Energy resolution: 6.2 keV (FWHM) @ 122 keV
Optics: Coded-mask (open fraction of 50%), size 2.7 m2
Detection area: 5240 cm2
Detector: CdZnTe (4 x 4 x 2 mm3)
# of detectors: 32,768 (256 module x 128 set)
Field of view: 120o x 90o
Localization accuracy: 1-4 arcmin
GRB detection: ~100 GRBs / year
128 CdZnTe

## Slide 7: XRT (X-ray telescope)
Optics: JET-X Wolter I (flight spare)
Focal length: 3.5 m
Effective area: 110 cm2 @ 1.5 keV
Detector: e2V CCD-22
Field of view: 23’ x 23’
Localization accuracy: ~ 5 arcsec
Energy range: 0.2 – 10 keV
Energy resolution: 190 eV @ 10 keV,
50 eV @ 0.1 keV
Sensitivity: 2 x 10-14 erg cm-2 s-1 @ 1000 s
X-ray mirror
X-ray CCD

## Slide 8: UVOT (Ultraviolet/Optical Telescope)
Optics: Aperture 30 cm (XMM OM’s spare)
Detector: MCP + CCD (same design as XMM OM)
Field of view: 17‘ x 17’
PSF: 0.9’ FWHM @ 350 nm
Observable wavelength: 170 – 600 nm
Filters: 7 filters + 2 grism
Sensitivity: 22.3 mag (white, 1000s)
Pixel size: 0.5 arcsec
V, B, U, UVW1, UVM2,
UVW2, White, UV-grism,
Optical-grism

## Slide 9: Swift autonomous GRB observation
BAT GRB detection: T0
GRB alert notice : T0 < 20 s
Slew the spacecraft to
the GRB location:
T0 + (20 – 75 s)
T0 < 300s
Optical image
1’
Prompt detection (BAT)
Localization: 1-5 arcmin
X-ray afterglow (XRT)
Localization: ~2-5 arcsec
X-ray image
T0 < 90 s
UV/optical afterglow (UVOT)
Localization: 0.5 arcmin

## Slide 10: BAT on-board trigger
Rate trigger
Image trigger
fg
bg
- 674 trigger criteria
- Each trigger criterion has a different trigger threshold
- ~80 triggers per day
+
Light curve
Sky image
Image significance ≧ 6.5
Trigger!
- Event data (~10 s) capture (low priority)
- Subthreshold triggers (available through GCN; require regular data downlink)
Trigger!
Image significance ≧ 7.0
Sky image
- Every 64 s
- 15-50 keV band only
- All the images are downloaded (high priority)
- Used in the BAT transient monitor (Krimm et al.)
Successful triggers:
Real time alert
Autonomous spacecraft slew
Event data capture: T0-250s –T0+1000s (high priority)

## Slide 11: Example of GRB 050713a
0.5 s exposure image
11 sigma detection

## Slide 12: GCN: Gamma-ray Coordinates Network
PI: S. Barthelmy (NASA/GSFC)
Operation: since 1990s -
99.7% livetime
>500 GCN Notice recipients
2127 GCN Circular recipients (2022/7)
Distribution of GRB detection information by various spacecrafts
Receiving and automatically distributing to the GRB community prose-style e-mail messages about follow-up observations on various GRBs
GCN Notices
GCN Circulars

## Slide 13: New GCN
GSFC: Judy Racusin, Leo Singer, … (after Scott’s retirement)

## Slide 14: Tracking and Data Relay Satellite System - TDRSS -
First generation TDRS
(launched: 1983-1995)
Second generation TDRS
(launched: 2000-2002)
Third generation TDRS
(launched: 2013-2017)
(TDRS-6, TDRS-7)
(TDRS-8, TDRS-9, TDRS-10)
(TDRS-11, TDRS-12, TDRS-13)
(figures and information from NASA TDRS webpage: https://www.nasa.gov/directorates/heo/scan/services/networks/tdrs_main)
Swift uses the 1 kbps DAS (Demand Access System) for the alert downlink and the ToO upload.
~70% of the time in orbit has a real-time communication between ground and space.
TDRSS will retire around 2025. NASA is aiming for transferring to a commercial communication service.

## Slide 15: Swift’s TDRSS data products
BAT
GRB BAT position notice
4 channel light curves (variable time scales)
‘Extended’ 4 channel light curves
ACS data
Scaled map (+ACS data)
XRT
XRT position notice
XRT light curve and image
Single pixel event (E > 0.5 keV; central 200 x 200 pixel in PC mode)
UVOT
UVOT 2x2 binned image
(“GeNi” image; 2 cycles of V and white filter)
All available through the GCN Notice

## Slide 16: BAT TDRSS data (GRB 061121)

## Slide 17: Swift’s TDRSS data products
BAT
GRB BAT position notice
4 channel light curves (variable time scales)
‘Extended’ 4 channel light curves
ACS data
Scaled map (+ACS data)
XRT
XRT position notice
XRT light curve and image
Single pixel event (E > 0.5 keV; central 200 x 200 pixel in PC mode)
UVOT
UVOT 2x2 binned image
(“GeNi” image; 2 cycles of V and white filter)
All available through the GCN Notice

## Slide 18
XRT Single Pixel Event Report (SPER) data
(https://www.swift.ac.uk/sper/)

## Slide 19: Swift’s TDRSS data products
BAT
GRB BAT position notice
4 channel light curves (variable time scales)
‘Extended’ 4 channel light curves
ACS data
Scaled map (+ACS data)
XRT
XRT position notice
XRT light curve and image
Single pixel event (E > 0.5 keV; central 200 x 200 pixel in PC mode)
UVOT
UVOT 2x2 binned image
(“GeNi” image; 2 cycles of V and white filter)
All available through the GCN Notice

## Slide 20
UVOT TDRSS images
UVOT white
DSS image

## Slide 21
Neil Gehrels

## Slide 22: The Neil Gehrels Swift Observatory
The Swift Gamma-Ray Burst Explorer has officially been renamed the Neil Gehrels Swift Observatory
Neil Gehrels (1952-2017)
Brad Cenko: Swift PI
Notes: Of course the primary purpose is to honor the leadership and vision of Neil. But the name was also chosen to reflect the fact that Swift does so much more than just gamma-ray bursts these days (indeed this is perhaps one of Neil’s most significant legacies).

## Slide 23: The very first story of Swift by Neil
around 36:26

## Slide 24: Swift’s discoveries

## Slide 25: 2004: Giant flare from SGR 1806-20
(Palmer et al. 2005)
December 27, 2004
- Swift was in the commitioning phase.
- Only BAT was operating (no XRT/UVOT)

## Slide 26: 2005: Short GRB Afterglow & High-z GRB
GRB 050509B: X-ray afterglow detection from a short GRB (Gehrels et al. 2005)
GRB 050904: Detection of a high redshift GRB (z=6.29) (Kawai et al. 2006)
The primary science objectives of Swift were detection of
an afterglow of a short GRB and,
a high redshift GRB.
Swift achieved those two primary science objectives within a year!

## Slide 27: 2005-2025: Mysterious X-ray afterglow lightcurve
(O’Brien et al. 2006)

## Slide 28: 2008: Supernova shock breakout in SN 2008D
(Soderberg et al. 2008)
FRED-like X-ray outburst (~400 s) at the onset of SN 2008D.
Total X-ray energy of the outburst: 2 x 1046 erg.

## Slide 29: 2008: Naked-eye burst GRB 080319B
(Racusin et al. 2008)

## Slide 30: 2011: Tidal disruption SwiftJ164449.3+573451
(Burrows et al. 2011)

## Slide 31: 2011: Ultra-long GRB 111209A
BAT triggered twice (trigger ID: 509336 & 509337).
(Stratta et al. 2013)
Prompt emission lasted for ~4 hours!
Time [s]

## Slide 32: 2017: Blue kilonova from GW 170817
(Evans et al. 2017)

## Slide 33: “Unique” capabilities of Swift

## Slide 34: Target of opportunity (ToO)
Failier of the thermal electric cooler
~90o
day
night
Swift
HETE-2/SVOM
Sun
Earth
GRB
GRB
Can’t heat the radiator by the earth and the sun to cool XRT
Swift GRBs are tend to be closer to the Sun.
Swift needs to passively cool the focal plane of XRT.
  Many slews with short durations by the pre-planned schedule.
What if a GRB happens?
  Need a rapid schedule change.
ToO

## Slide 35: Various ToO capabilities
Easy to request a ToO
Tiled observation
Many pointing
Those additions required a flight software change. But they are done promptly because the software was written by the BAT team scientist, David Palmer.
David Palmer

## Slide 36: BAT flight software log file

## Slide 37: All the data are publicly available immediately
All the data became publicly availale around mid April 2005 (~5 months after the launch).
  Instrument calibration (Crab observations)
  Validation of the data (cross-calibration)
  Science software (debugging)
  Documentation (try not the users doing a supid thing)
Swift team members were unhappy:
- many scooped articles were published…
The immediate public data produce a lot more science!

## Slide 38: High redshift GRBs

## Slide 39: Swift known-z GRB samples
BAT GRB catalog
  Total # of GRBs: 1668 (from GRB 041217 to GRB 250605A)
  Total # of known-z GRBs: 531
  z > 6 GRBs
    GRB 050904: z=6.295
    GRB 060116: z=6.6
    GRB 080913: z=6.733
    GRB 090423: z=8.26
    GRB 090429B: z=9.38
GRB 100905A: z=7.88
GRB 120923A: z=7.84
GRB 140515A: z=6.33
GRB 210905A: z=6.318
GRB 240218A: z=6.782

## Slide 40: BAT light curve (15-350 keV) of z>6 GRBs
GRB 050904: z=6.295
GRB 060116: z=6.6
GRB 080913: z=6.733
GRB 090423: z=8.26
GRB 090429B: z=9.38
GRB 100905A: z=7.88
GRB 120923A: z=7.84
GRB 140515A: z=6.33
GRB 210905A: z=6.318
GRB 240218A: z=6.782
Time since the BAT trigger [s]
Time since the BAT trigger [s]

## Slide 41: Prompt duration/fluence vs. redshift
T90 [s]
Redshift
S(15-150 keV) [erg/cm2]
Redshift

## Slide 42: Empirical spectral models of GRBs
Ea exp (-E/E0)
Eb
E0 = Epeak / (2 + a)
Ebreak = (a - b) E0
Band function
dN/dE
Energy
David Band (1957-2009)
(Band et al. 1993)
(α ~ -1)
(β ~ -2.5)

## Slide 43: Photon index α / 1-s peak flux vs. redshift
a
Redshift
Redshift
P1s (15-150 keV) [erg/cm2/s]

## Slide 44: BAT on-board trigger v.s redshift
Foreground trigger duration [s]
Redshift
Redshift
15-50 keV
25-100 keV
50-350 keV

## Slide 45: GRB X-ray afterglow light curve
0.3-10 keV energy flux [erg/cm2/s]
Time since the BAT trigger [s]

## Slide 46: Smallsat development at AGU

## Slide 47: ARICA-2: AGU Remote Innovative Cubesat Alert System-2
(天体の“ありか”を速報する)
7/28-8/2 Thermal-vac
ARICA-2 FM
Delivery: November 2025
Launch: FY 2025

## Slide 48: SEAGULL: SEArching origin of Gravitational wave source by cube sateLLite
(Sei-san’s poster)
- Dedicated X-ray counterpart search for GW sources
- Target launch around GW O5

## Slide 49: Future of Swift
Time since 2025 [yr]
Altitude [km]
Altitude < 300 km
-> just before year 2028
NASA’s “stupid” presidental budget
Swift orbit

## Slide 50: Summary
Swift revolutionalized our understanding of transient universe.
Swift marked 20 years, and still counting. More operation, more discovery.
Flexible (software oriended) design saved the Swift operation.
z > 6 GRBs are very rate in the Swift sample. The hard X-ray band is probabliy not the best wavelength to hunt high-z GRBs.
The Swift hardwares are working well. Either the orbit or the budget will limit the operation.

## Slide 52: The Swift Song
(Words and music by Padi Boyd)

## Slide 53: My relationship to Neil
2004 | March | Received Ph.D. (Tokyo Tech)
2004 | October | NRC postdoc at GSFC/NASA (Supervisor: Neil)
2004 | November | Swift launch
2004 | December | Marriage
2007 | October | Research associate at CRESST/UMBC/GSFC
2007 | November | Mayuko’s birth
2010 | October | Yuiko’s birth
2012 | September | Assistant professor at Aoyama Gakuin U. (non tenure)
2017 | April | Associate professor at Aoyama Gakuin U. (tenure)
2004-2012 (8 years at GSFC): Neil was my mentor during
an initial post-doc period and a starting of my new family life.

## Slide 54: In orbit issues

## Slide 55: BAT: Issues
Numbers of enabled detectors
Lien et al. 2014
~15800 detectors enabled (as of Aug 4, 2025)
Reduce the sensitivity (smaller effective area)
Gain change of CdZnTe detectors
241Am spectrum: array averaged
1.5 (early) - 0.4 (current) keV/yr shift in 59.5 keV line (array averaged).
The pulse width seems getting wider.
Implimented in the BAT ground softwares (CALDB).

## Slide 56: XRT: Issues
Failier of the thermal electric cooler
~90o
day
night
Swift
HETE-2/SVOM
Sun
Earth
GRB
GRB
Can’t heat the radiator by the earth and the sun to cool XRT
Micro-meteorite strike (May 2005)
Swift GRBs are tend to be closer to the Sun.
Kennea et al. 2020
5 hot columns were formed (the two in the middle of the detector)
Care is needed if your source is in the dead column.

## Slide 57: Neil as a mentor
E-mail from Neil on December 21, 2016:
Always supported and encouraged my works.
Always gave me the best environment to focus on the works.
Never let me involved in a (dirty) political work.
Always concerned about my family.
Neil:
Notes: I start to have my own small research group at AGU and supervise students. I will never forget Neil’s attitude as a mentor, and I will try my best for the students to have a similar feeling what I received from Neil.